## Slide 1
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
MPM Ready to Receive
Upstream No Board Available
Downstream Ready to Receive
MPM No Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
As all 3 machines are placed into Production Mode, the following occurs.
The MPM & Downstream machines respectively should close contacts B and D to indicate they are Not Busy. They then monitor respective contacts A and C for closure. A board is placed on the Input track sensor at position 1 of the Upstream machine and is immediately moved toward position 2.
Single Track MPM Printer Board Transfer

## Slide 2
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
Upstream Board Available
MPM No Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
As the board reaches the Output sensor (position 2), the Upstream machine closes contact A and checks to see if contact B of the MPM is closed. If it is, then board transfer begins.
MPM Ready to Receive
Downstream Ready to Receive

## Slide 3
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
Upstream No Board Available
MPM No Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
As the board moves from the Upstream machine onto the MPM printer, closed contacts (A and B) must open for at least 50ms before another board can transfer.
# Opening time of contact A during the transfer sequence varies by machine manufacturer
* For the MPM, if Standard SMEMA is set, contact B opens as soon as the transfer begins
If Extended SMEMA is set, contact B opens when the board’s leading edge reaches position 3 sensor. If Extended SMEMA 2 is set, contact B opens when the board’s trailing edge passes position 3 sensor.
*
MPM Ready to Receive
Downstream Ready to Receive

## Slide 4
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
MPM Busy
Upstream No Board Available
MPM No Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
With the transfer sequence complete, the board continues toward the print area (position 4). There the board elevates and printing commences. After printing is complete, the board lowers and is moved toward position 5.
Downstream Ready to Receive

## Slide 5
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
MPM Busy
Upstream No Board Available
MPM Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
As the board arrives at position 5, contact C closes. The MPM checks for a closed contact at D on the Downstream machine. If it is, then both machines initiate a board transfer to move the board toward position 6.
Downstream Ready to Receive

## Slide 6
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
MPM Busy
Upstream No Board Available
MPM Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
As the board starts to move toward position 6, the MPM maintains contact C closed until sensor 5 no longer detects the board. The Downstream machines closed contact D timing varies by manufacturer.
Downstream Ready to Receive

## Slide 7
Upstream Machine
MPM Printer
Downstream Machine
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
1
2
3
4
5
Upstream No Board Available
Downstream Busy
MPM No Board Available
A#
B
C
D
24 VDC
1
2
3*
4
5
6
7
With the transfer complete contact B of the MPM printer closes to let the Upstream machine know it is Not Busy and monitors contact A for the Board Available signal.
MPM Ready to Receive